## Slide 1
Digital Implementation Trade-offs in PID-Controlled Buck-Boost Converters
A Simulation-Based Study of Sampling and Quantization Effects
Presented by: Syeda Salsabil Islam Ariya & Jasimul Islam Chowdhury
Presented to: Tareq Anwar Shikdar

## Slide 2
1. Background & Motivation
• Buck-boost converters are widely used where the input voltage may be above or below the required output voltage.
• PID control offers a simple and practical approach for closed-loop voltage regulation.
• An ideal Simulink controller does not fully represent a real digital implementation.
• Digital control introduces discrete sampling, finite measurement resolution and finite PWM/duty-cycle resolution.
• These limitations can affect transient response, steady-state accuracy, ripple and small persistent oscillations.
• This study will quantify these effects using the PID-controlled buck-boost converter that has already been developed.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 2

## Slide 3
2. Literature Review
• Digital PID control of buck-boost converters has already been studied. Earlier work used discrete PID structures together with ADC and DPWM concepts and evaluated the controller through simulation and hardware.
• Research on digital DC-DC control also shows that sampling frequency, discretization and implementation delay influence closed-loop performance.
• A 2020 study examined analog and digital PID/PIDN control of a bidirectional buck-boost converter using MATLAB-based analysis.
• Therefore, simply converting the existing PID controller into a discrete controller would not provide sufficient novelty.
• Our study instead focuses on a systematic, design-oriented investigation of practical digital implementation limitations.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 3

## Slide 4
3. Literature Review — Quantization & Research Gap
• González-Castaño et al. (2020) investigated ADC quantization and DPWM-related quantization-induced perturbations in a digitally controlled buck-boost converter.
• Their work used a two-loop current-controlled architecture, a coupled-inductor converter, analytical investigation, simulation and experimental validation.
• A recent 2025 study further investigated end-to-end ADC/DPWM quantization co-design for MHz GaN converters across several converter topologies.
• These studies establish that quantization itself is not a new topic.
• Proposed gap: a focused study of the combined influence of sampling time, ADC/measurement resolution and PWM resolution in a simple single-loop voltage PID buck-boost architecture, with emphasis on practical performance boundaries.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 4

## Slide 5
4. Research Questions & Objectives
Research Questions
• How does sampling time affect transient and steady-state performance?
• How do ADC and PWM resolutions affect regulation accuracy and ripple?
• What is the combined effect of sampling and finite digital resolution?
• Can a practical range of sampling speed and digital resolution be identified?
Objectives
• Validate the existing PID buck-boost model as the baseline.
• Separately investigate sampling, ADC resolution and PWM resolution.
• Evaluate their combined effects under nominal and selected disturbance conditions.
• Quantify performance and identify practical implementation limits.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 5

## Slide 6
5. Proposed System & Research Framework
Vref
Error
Σ
PID
PWM /
DPWM
Buck-Boost
Converter
Vout
Sampling +
ADC
• Existing power stage and PID controller remain the starting point.
• Only standard Simulink blocks such as sampling/hold and Quantizer will be added.
• No PSO, ANN, LSTM, fuzzy controller or new converter topology is required.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 6

## Slide 7
6. Methodology — Step 1: Establish the Baseline
1. Record the existing converter parameters: Vin, Vref, L, C, load, switching frequency and PID Kp, Ki, Kd.
2. Run the existing PID-controlled model under nominal operating conditions.
3. Verify stable output-voltage regulation.
4. Record Vout, inductor current, duty ratio and error.
5. Calculate settling time, overshoot, steady-state error, ripple, IAE and ITAE.
6. Save this as the reference/ideal case.
7. All later simulations will use identical converter parameters unless the investigated variable is intentionally changed.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 7

## Slide 8
7. Methodology — Step 2: Sampling & ADC Resolution
Sampling study:
• Insert a discrete sampling/hold stage in the feedback path.
• Keep ADC and PWM resolution effectively ideal while sampling is investigated.
• Test sampling periods relative to the switching period, e.g. Tsw, 2Tsw and 5Tsw; final values depend on the actual model.
ADC study:
• Keep sampling time fixed.
• Model finite measurement resolution with a standard Quantizer/equivalent block.
• Test practical resolutions such as 12-, 10-, 8- and 6-bit, subject to the actual voltage range and model behavior.
• Compare regulation accuracy, ripple and transient metrics.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 8

## Slide 9
8. Methodology — Step 3: PWM & Combined Effects
PWM-resolution study:
• Keep sampling time and ADC resolution fixed.
• Represent finite duty-cycle resolution in the PWM command.
• Test selected PWM resolutions such as 12-, 10-, 8- and 6-bit.
Combined study:
• Combine selected sampling times, ADC resolutions and PWM resolutions.
• Use a small, controlled test matrix rather than hundreds of simulations.
• Determine whether performance degradation is mainly caused by sampling, measurement resolution, PWM resolution, or their interaction.
• Inspect steady-state waveforms for persistent quantization-induced oscillation.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 9

## Slide 10
9. Methodology — Step 4: Disturbance Tests & Metrics
Disturbance tests:
• Nominal operation with fixed Vin and load.
• Input-voltage step within the converter's safe operating range.
• Load step within the model's valid operating range.
• Selected repeated transitions for the most informative configurations.
Performance metrics:
• Settling time and overshoot.
• Steady-state error and RMS voltage ripple.
• IAE = ∫|e(t)|dt and ITAE = ∫t|e(t)|dt.
• Limit-cycle amplitude = Vmax,ss − Vmin,ss.
• Efficiency only if reliable input/output power data are already available.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 10

## Slide 11
10. Expected Results, Contribution & Novelty
Expected findings to be tested:
• Slower sampling and coarser resolution are expected to increase regulation error and/or oscillatory behavior.
• A practical region should exist where performance remains close to the reference controller.
• The interaction between sampling and finite resolution may reveal combinations that are unnecessarily expensive or unnecessarily restrictive.
Expected contribution:
• A reproducible Simulink framework for single-loop PID buck-boost digital implementation analysis.
• Quantitative comparison of sampling, ADC and PWM limitations.
• A practical performance map showing acceptable implementation regions.
• The novelty is the focused combined, design-oriented characterization—not the claim that quantization itself is new.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 11

## Slide 12
11. Proposed Paper Structure & Core References
Paper structure:
• I. Introduction
• II. Related Work and Research Gap
• III. Buck-Boost Converter and PID Model
• IV. Digital Implementation Model
• V. Simulation Methodology
• VI. Results and Discussion
• VII. Practical Performance Map / Guidelines
• VIII. Conclusion
Core references:
• Vijayalakshmi & Sree Renga Raja, 2014 — digital PID buck-boost control.
• González-Castaño et al., Applied Sciences, 2020 — ADC quantization and digital buck-boost control.
• Journal of Electrical Systems and Information Technology, 2020 — digital PID/PIDN bidirectional buck-boost control.
• Recent 2025 work — end-to-end ADC/DPWM quantization co-design for MHz GaN converters.
Research Proposal | Ariya & Jasimul Islam Chowdhury | 12